## Slide 1: Preliminary Design Review Automated Wheelchair
Max Bronson
Oscar Montealegre
Denny Mannakulathil

## Slide 2: System Overview
An Autonomous wheelchair that will implement LIDAR and a Kinect Camera to maneuver through the world
Python based data interpretation and navigation
Controlled with a user provided laptop and Arduino 2560 Rev3

## Slide 3: Block Diagram
Velodyne VLP-16
LiDAR Sensor
Dell Latitude 7285
Laptop
Arduino MEGA 2560 Rev3
Right Motor
MX2206-9
Kinect V2 (Model 1520)
Left Motor MX2206-9
Joystick

## Slide 4: Major Parts
Part | Model | Purchased
Frame | Standard motor driven wheelchair with battery | ✔
Microcontroller | Arduino Mega | ✔
Sensors | Velodyne VLP-16, Microsoft Kinect V2 | ✔
Laptop | Dell Latitude 7285 | ✔
Battery | Bioenno Power Lithium Ion Battery | ✔

## Slide 5: Major Works
Mechanical assembly completed 35%
  Wheelchair base and wiring box are assembled
  Laptop mount is being 3-D printed, sensor mounts in design phase
Electrical system completed 60%
  All parts have been acquired
  Wiring of digital logic between Arduino and wheelchair is complete
  Wiring of power and digital signals between sensors laptop and Arduino still to be completed.
Programming completed 30%
  ROS packages have been acquired and interfacing with major sensors has been confirmed. Conversion of data transmitted to useable information for Wheelchair still to be completed.

## Slide 6: Design Requirements & Specifications

## Slide 7: Design Requirements & Specifications

## Slide 8: Design Requirements & Specifications
Functions
Avoid both stationary and moving object while navigating
Navigate from start point to finish point autonomously
Path plan and adjust plan using new data collected
Implement SLAM to map the surrounding world

## Slide 9: Dimensions
Avoid both stationary and moving object while navigating
Navigate from start point to finish point autonomously
Path plan and adjust plan using new data collected
Implement SLAM to map the surrounding world

## Slide 10: Supporting Video

## Slide 11: VLP-16 Dimensions

## Slide 12: Sensor Diagrams

## Slide 13: Basic Design & Trade Study Results
Microcontrollers
Sensors
Battery
Structure

## Slide 14: Microcontrollers
Arduino Mega 2560 Rev3
54 digital I/O pins (15 PWM output)
16 analog input pins
4 UARTs (hardware serial ports)
16 MHz Crystal Oscillator (processor)
8 kB of on-board RAM
256 kB of memory
101.52mm X 53.3mm, 37 grams
Source: https://store.arduino.cc/usa/arduino-mega-2560-rev3

## Slide 15: Linux Workstation
Dell Latitude 7285
2-in-1 laptop tablet combination
Intel Core 7th Generation i7-7Y57 Processor
16GB LPDDR3 Memory
12.3" Screen
.28" X 10.8" X 8.2", 680 g
Source: https://www.dell.com/

## Slide 16: Linux Machine Weighted Rating Trade Study
Criteria | Weight | Dell Latitude 7285 |  | Raspberry Pi 3.0 | 
 |  | Rating | Weighted | Rating | Weighted
Processor Speed | 0.5 | 4 | 2.0 | 3 | 1.5
Usability | 0.10 | 5 | 0.5 | 3 | 0.3
Memory | 0.2 | 4 | 0.8 | 2 | 0.4
Form Factor | .1 | 2 | 0.2 | 5 | 0.5
Total | 1 |  | 3.5 |  | 2.7

## Slide 17: Sensors
Velodyne VLP-16
  LiDAR (Light Detection & Ranging) Sensor
Microsoft Kinect V2
  Infrared, RGB sensors & Microphone Array

## Slide 18: LIDAR Weighted Rating Trade Study
Criteria | Weight | Velodyne VLP-16 |  | MS Kinect V2 | 
 |  | Rating | Weighted | Rating | Weighted
Range | 0.25 | 5 | 1.25 | 2 | 0.5
Frequency | 0.35 | 3 | 1.05 | 2 | 0.7
Angular Range | 0.3 | 4 | 1.2 | 3 | 0.9
Cost | 0.1 | 5 | 0.5 | 5 | 0.5
Total | 1 |  | 4.0 |  | 2.6

## Slide 19: LiDAR & Kinect Battery
Bioenno Power Lithium Iron Phosphate Battery
Capacity - 20 Ah
480 Watt-Hours
Amps - 40 A
Voltage - 12 V
Type - Lithium Iron Phosphate (LiFePO4)
Dimensions – 9.5" X 5.5" X 3.5", 2.4kg
Source: https://powerwerx.com/

## Slide 20: Battery Weighted Rating Trade Study
Criteria | Weight | Bioenno 12V |  | Eco-Worthy 12V | 
 |  | Rating | Weighted | Rating | Weighted
Weight | 0.2 | 3 | 0.6 | 4 | 0.9
Amps | 0.1 | 3 | 0.3 | 3 | 0.3
Size | 0.2 | 4 | 0.8 | 2 | 0.4
Cost | 0.5 | 5 | 2.5 | 2 | 1.0
Total | 1 |  | 4.2 |  | 2.6

## Slide 21: Wheelchair Structure
Seat Height: 19 in.
Seat Depth: 19 in.
Back Height: 36 in.
Width: 23 in.
Rear Wheel Radius: 4.75 in.
Front Wheel Radius: 3 in.
One 120 watt motors mounted
    on each back wheel
Material: Aluminum with cloth seat

## Slide 22: Frame Weighted Rating Trade Study
Criteria | Weight | Yurob Portable |  | Electra 7 |  | Falcon Portable | 
 |  | Rating | Weighted | Rating | Weighted | Rating | Weighted
Weight | 0.2 | 4 | 0.8 | 2 | 0.4 | 2 | 0.4
Foot Print | 0.2 | 3 | 0.6 | 2 | 0.4 | 2 | 0.4
Motor Interface | 0.3 | 4 | 1.2 | 3 | 0.9 | 3 | 0.9
Cost | 0.3 | 5 | 1.5 | 2 | 0.6 | 3 | 1.0
Total |  |  | 4.10 |  | 2.30 |  | 2.70

## Slide 23: Verification Approach/Plan
Analysis
  Path planning analysis
  Modify path planning and obstacle avoidance algorithms
Simulation
  SolidWorks Models of 3D printed parts
  Obstacle avoidance Gazebo
Test
  Testing of sensors prior to implementation
  Testing of wheelchair using Joystick
  Obstacle avoidance testing in the real world

## Slide 24: Verification Approach/Plan (cont.)
Systems​ | Analysis​ | Model​ | Simulation​ | Testing​
Mechanical​ | ✔​ | ✔​ | ✔​ | ✔​
Motors​ | ​ | ​ | ​ | ✔​
Batteries​ | ✔​ | ​ | ​ | ✔​
Microcontroller​ | ✔​ | ​ | ​ | ✔​
Sensors​ | ✔​ | ​ | ✔​ | ✔​

## Slide 25: Design & Development
Avoid both stationary and moving object while navigating
Navigate from start point to finish point autonomously
Path plan and adjust plan using new data collected
Implement SLAM to map the surrounding world

## Slide 26: Digital Wiring Diagrams

## Slide 27: Power Wiring Diagrams

## Slide 28: Velodyne PointCloud

## Slide 29: Kinect RGB & Infrared Visualization

## Slide 30: Bill of Materials
Description | Quantity | Cost per Unit | Cost Total
Electric Wheelchair | 1 | $1,000.00 | $1,000.00
LIDAR | 1 | $4,000.00 | $4,000.00
Kinect Camera | 1 | $40.00 | $40.00
Bioenno Battery | 1 | $193.00 | $193.00
Mounting Hardware | 1 | $53.00 | $53.00
Arduino 2560 | 1 | $40.00 | $40.00
Electrical Wires Multipack | 1 | $16.00 | $16.00
Resistor Multipack | 1 | $12.00 | $12.00
Dell Latitude 7285 | 1 | $1,200.00 | $1,200.00
Bread board | 1 | $5.00 | $5.00
Total |  |  | $6559

## Slide 31: Minimum Success Criteria
Navigate to a target point with an error of less than or equal to 4 Feet.
Avoid wall and stationary objects in desired path not moving closer than 2 feet.
Avoid a moving object that passes in front of the wheelchair while navigating to the target point using LiDAR and Kinect for object recognition.
Will be able to navigate to a point 50 feet away at a minimum rate of 3 mph.

## Slide 32: Design Optimization/Improvements
Voice command recognition using Kinect Microphone and python packages
Manual joystick replacement
Alternative path planning algorithms
Improve wiring of digital signals
Exhaustive obstacle avoidance (including variation in elevation)

## Slide 33: Resources
Mentors Chris Voicu Facility Engineering Lab Q-118 Senior Design Lab | Hardware LIDAR Sensor Ultrasonic Sensors Arduino MEGA Wheelchair Frame Kinect Camera Dell Latitude 7285 Software Solidworks AutoCAD Electrical Ubuntu 20.04 C++/Python/ROS

## Slide 34: Project Budget
Item(s) | Price ($)
Sensor Adapters | $30
Battery Mount Hardware | $40
Sensor Mount Hardware | $30
Misc Parts/Material | $50
Total (with contingency) | $150

## Slide 35: Schedule

## Slide 36: Team Chart
Max Bronson – Team Lead, LiDAR Interfacing, ROS & Arduino Programming
Denny Mannakulathil – Solidworks Modeling, 3-D Printing, Mechanical Assembly
Oscar Montealegre – Kinect Interfacing, Object Identification, ROS programming

## Slide 37: References/Major Data Sheets
References
  LiDAR reference 1
  Autonomous wheelchair reference
  OpenCV reference
  Python reference
  Solidworks reference 1
  Solidworks reference 2
  Solidworks reference 3
  Solidworks reference 4
Data Sheets
  LIDAR Datasheet
  Kinect Datasheet
Notes: Possibilities:
Raspberry Pi Manual
Lidar Technical Sheet
Pixhawk PX4 Manual
ETC